## Slide 1
FPGA Fundamentals

## Slide 2
What is an FPGA?
Field Programmable Gate Array.
Contains:
  Logic gates
  Registers
  Configurable Routing
  Memory (RAMs, ROMs)
  PLLs
  Arithmetic & DSP
  Hard IP Blocks
Fully programmable.

## Slide 3
Configurable Logic Block (CLB)
Look Up Table
D Type
Flip Flop
MUX
Clock
Reset
A
B
C
D
F
CLB

## Slide 4
Simplified FPGA Architecture
FPGA IO PINS
IO
IO
IO
IO
IO
PLL
RAM
CLB
Programmable Routing
CLB
CLB
CLB

## Slide 5
Why Use An FPGA?
Used for implementing Digital Systems.
Extremely Flexible.
  No limit to timers, counters, peripherals etc.
  Does not have a fixed hardware structure.
  Change whole design without changing layout.
Very fast.
Parallel processing (Doesn’t execute sequentially).
Large bandwidth (Data width configurable).
Intensive data processing (Video, DSP, FFT etc)

## Slide 6
When Not To Use An FPGA
In cost sensitive applications.
Carrying out infrequent tasks that are sequential in nature (eg : search / sort algorithms).
When speed and latency are not that important.

## Slide 7
FPGA Programming
Hardware Descriptive Languages (HDL)
C/C++ using HLS (High Level Synthesis)
Popular HDL Languages :
VHDL | Verilog
Strongly Typed | Weakly Typed
Deterministic | Only Deterministic If you Follow Rules Carefully.
Verbose | Concise
Non C Like Syntax | More C Like Syntax

## Slide 8
Behavioural Vs RTL
RTL
Synthesisable
Behavioural
Not Synthesisable
VHDL

## Slide 9
RTL (Register Transfer Level)
Can be simulated, synthesised & implemented on an FPGA.
Describes hardware in terms of registers and combinational logic that sits between them.
Need to have an idea of the digital circuit.
No explicit delays.
All timing described in terms of clock edges.
Used as input to a synthesis tool.

## Slide 10
Behavioural
Can only be simulated. Cannot be synthesised.
Can have explicit delays,
Uses an algorithm to describe functionality.
Describes behaviour at a higher level.
Used to build a verification model to simulate the behaviour of a system or module.
Used for simulation purposes for example in writing test benches.

## Slide 11
FPGA Design Flow
Start from the Design Specification
Use VHDL Editor To :
  Write VHDL (RTL)
  Write Test-Bench (RTL + Behavioural)
Simulate to ensure correct behaviour.
Write Timing Constraints.
Synthesis tool to generate a netlist.
Implementation tool to take netlist and perform placement, routing and optimisation.
Make sure designs meets Timing. If not go back to VHDL code.
Implementation creates a binary file used to configure the FPGA.

## Slide 12
FPGA Design Flow
Program binary file into FPGA configuration flash (using JTAG for example)
FPGA
Config Flash
JTAG Programmer
JTAG Port

## Slide 13
Chapter Summary
Configurable Logic Block (CLB)
FPGA Architecture
When to use an FPGA?
What are FPGAs good at?
When might you not use an FPGA?
Overview of FPGA programming languages.
Typical FPGA design flow.